## Slide 1
SPI project Report
Reporter：Haining Sun, Xiaochong Huang
Mentor：Jian Cao，Song Ma

## Slide 2
01.
Introduction to ports and registers
03.
DC simulation and post-simulation
02.
Simulation waveform
04.
Backend and testing
目录
contents

## Slide 3
01
Introduction to ports and registers

## Slide 4: 1.1 Port definition
input | width | function | output | width | function
clk | 1 | system clock | sfr_data_o | 8 | output register
rst_n | 1 | reset(active low) | spssn_o | 8 | spi slave select
sfraddr_w | 2 | write addr | inout | width | function
sfrwe | 1 | write enable | mosi | 1 | master output slave input
spidata_i | 8 | write data | miso | 1 | master input slave output
sfraddr_r | 3 | read addr | sck | 1 | spi clock
spssn_i | 8 | spi slave select | ssn | 1 | slave select

## Slide 5: 1.2 Register definition
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  | SPE |  | MSTR | CPOL | CPHA |  | 
W |  |  |  |  |  |  |  | 
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
addr_w = 00 : spicr1
addr_r = 000
SPE : spi enable
MSTR: mstr = 1, master mode; mstr = 0, slave mode
CPOL: clock polarity control bit
CPHA: clock phase control bit

## Slide 6: 1.2 Register definition
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  |  |  |  |  |  |  | 
W |  |  |  |  |  |  |  | 
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
addr_w = 01 : spicr2
addr_r = 001
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  | SPPR2 | SPPR1 | SPRR0 |  | SPR2 | SPR1 | SPR0
W |  |  |  |  |  |  |  | 
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
addr_w = 10 : spibr
addr_r = 010
Reserved

## Slide 7: 1.2 Register definition
addr_w = 11 : spidr1
addr_r = 100
addr_r = 011 : spisr
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  |  |  | intspi |  |  | data_finish_s | data_finish_m
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Data to be transferred
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  |  |  |  |  |  |  | 
W |  |  |  |  |  |  |  | 
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 8: 1.2 Register definition
addr_r = 101
received data
 | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | Bit 0
R |  |  |  |  |  |  |  | 
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 9
02
Simulation waveform

## Slide 10: 2.1 Testbench
Instantiate a master and a slave respectively, and connect the interfaces to transmit data
Notes: 赋值的时序逻辑，提供的激励：
1.首先对寄存器进行赋值，之后给出spssn信号。
2.主从模式切换，保证模式测试完备。

## Slide 11: 2.2 Simulation waveform

## Slide 12: 2.2 Simulation waveform
Mode 0 : cpol = 0, cpha = 0. In idle state SCK is low.
data being latched on odd numbered edges and shifted on even numbered edges
Mode 1 : cpol = 0, cpha = 1. In idle state SCK is low.
data being latched on even numbered edges and shifted on odd numbered edges

## Slide 13: 2.2 Simulation waveform
Mode 2 : cpol = 1, cpha = 0. In idle state SCK is high.
data being latched on odd numbered edges and shifted on even numbered edges
Mode 3 : cpol = 1, cpha = 1. In idle state SCK is high.
data being latched on even numbered edges and shifted on odd numbered edges

## Slide 14
03
DC simulation and post-simulation

## Slide 15: 3.1 timing report

## Slide 16: 3.2 post simulation waveform
Backannotate and simulation with netlist.
Consistent with pre simulation results

## Slide 17
04
Backend and testing

## Slide 18
THANKS TO THE TEACHER'S CAREFUL GUIDANCE